## Slide 1: WP5: Cleopatra Connecting Locations of ESFRI Observatories and Partners in Astronomy for Timing and Real-time Alerts
Arpad Szomoru
Joint Institute for VLBI ERIC (JIVE)
On behalf of the Cleopatra collaboration

## Slide 2
Euclid
EGO/Virgo
WP5: Cleopatra
Connecting real facilities now as path to connected future facilities
~2.5 M€, 4 tasks
12 partners: JIVE, VU, UGR, NIKHEF, SURFnet, ASTRON, UVA, DESY, CNRS-APC, IEEC, GTD, STFC

## Slide 3: Objectives
It’s all about connectivity:
Timing: enable and improve long-haul many-element time and frequency transfer over optical fiber networks
Develop methods for rapidly relaying alerts between facilities, formulate scientific strategies, enabling joint observations of transient events
Handling of large data streams: leverage the e-VLBI experience to develop user-friendly, transparent and robust data streaming software
Scheduling of complex multi-element instruments, joint scheduling of multiple facilities around the globe, using advanced scheduling algorithms

## Slide 4: Task 1: Synchronization VU, ASTRON, JIVE, UGR, FOM, DESY, SURFnet (Koelemeij, Berge)
Time and frequency transfer on optical fiber networks through White Rabbit Ethernet (WRE)

## Slide 5: What is White Rabbit?
Atomic clock
White Rabbit Ethernet (CERN, based on IEEE Precision Time Protocol)
Time, frequency, and 1 Gb/s data in one
1 PPS, 10 – 125 MHz
Designed for 1 ns timing over distances <10 km (LHC, CERN)
Commercially available

## Slide 6: Task 1: Synchronization (continued)
Alternative to the intricate and custom-built timing solutions used in previous neutrino telescopes and many radio telescope arrays
Enable highly synchronized real-time observations by widely separated instruments, providing a unique "multi-messenger” view of astrophysical phenomena
Commercial applications: back-up or augment timing and navigation through the Global Navigation Satellite Systems
  Centimeter-level positioning for indoor navigation
  Autonomous vehicles using hybrid optical/wireless networks

## Slide 7: WRE and VLBI: a demo
Need three orders of magnitude improvement in frequency stability
Bi-directional light paths on operational fiber-optic telecommunication networks
New calibration and characterization tools
  Under harsh conditions

## Slide 8
WRE
node
Tx
Rx
Westerbork
Dwingeloo (ASTRON)
WRE
node
Tx
Rx
Clean-up
oscillator
25 km
Time & frequency for
VLBI
H-maser
Correlator
Existing data link
New data
link
WSRT
CAMRAS

## Slide 9
WRE
node
Tx
Rx
H-maser
Westerbork
Dwingeloo (ASTRON)
Correlator
Existing data link
New data
link
WSRT
CAMRAS
OSC Rx
OSC Tx
OEO
DWDM
node Tx
OSC Tx
OSC
band
C-band
OEO
OSC Tx
DWDM
node Tx
OSC Rx
OSC Tx
OEO
OSC Rx
OEO
DWDM
node Rx
Groningen
Assen
DWDM
node Rx
OSC Rx
OSC
band
C-band
WRE
node
Tx
Rx
Clean-up
oscillator
2×55 km
2×45 km
25 km
C-band
C-band
C-band
C-band
Time & frequency for
VLBI

## Slide 10
WRE
node
Tx
Rx
Westerbork
Dwingeloo (ASTRON)
OSC Rx
OSC Tx
OEO
DWDM
node Tx
OSC Tx
OSC
band
C-band
OEO
OSC Tx
DWDM
node Tx
OSC Rx
OSC Tx
OEO
OSC Rx
OEO
DWDM
node Rx
Groningen
Assen
DWDM
node Rx
OSC Rx
OSC
band
C-band
WRE
node
Tx
Rx
Clean-up
oscillator
2×55 km
2×45 km
25 km
C-band
C-band
C-band
C-band
Time & frequency for
VLBI and LOFAR
H-maser
WRE
switch
Tx0
Rx0
Tx1
Rx1
Rx2
Tx2
LOFAR CN
Buinen
Tx
Rx
WRE
node
65 km
DF
Correlator
Existing data link
New data
link
WSRT
CAMRAS
Clean-up
oscillator

## Slide 11: Task 2: Multi-messenger methods JIVE, ASTRON, CNRS-APC, UVA (Kettenis)
Develop standards for generation, dissemination, distribution and response to transient events (based on VOEvents)
Demonstration during which e.g. radio facilities like LOFAR, EVN, follow up a GW event
Investigate scientific synergies for automated follow-up observations

## Slide 12: Possible targets
Fast Radio Bursts
Flare stars
X-Ray Binary outbursts
Gamma-ray bursts
Supernovae
Neutrino triggers
Unknown
…
?
Notes: FRBs important.

## Slide 13: Gravitational waves: GW 150914
Two black holes
Distance of ~400 Mpc
Masses of 36 and 29 M
3 M of energy released
Abbott et al. (2016a)

## Slide 14: Multi-wavelength follow-up
Majority of localisation region covered at each wavelength
Follow-up teams used a range of strategies
Abbott et al. (2016b)

## Slide 15: Task 3: User-domain data streaming JIVE (Verkouter)
High-throughput data transfer utilities mostly use TCP:
  Abysmal performance on long-haul links
  some commercial tools use UDP but these are very expensive
Local experience both with lossy real-time and reliable near-real-time data
But, (e-)VLBI software is way too specialized and non-standard for simple file-to-file transfers
Developing open-source file transfer utility using the UDT protocol
  Reliable, robust, user-friendly

## Slide 16: Task 4: Scheduling of large astronomical infrastructures IEEC, STFC, GTD (Colome)
Complex, many-element detector arrays
  SKA, CTA

## Slide 17: CTA observation modes
Deep field
~1/2 of telescopes
Deep field
~1/3 of telescopes
Monitoring
4 telescopes
Monitoring
4 Telescopes
Monitoring
1 telescope
Monitoring
4 telescope
Divergent & convergent mode in
SUB-ARRAY configuration

## Slide 18: Task 4: Scheduling of large astronomical infrastructures (continued)
Artificial Intelligence (AI) techniques to optimize procedures
  Metaheuristic Optimization: Genetic Algorithms, Multi-objective Evolutionary Algorithms
  Constraint-Based Reasoning: constraint propagation
Maximize science return of SKA and CTA
  But ensure solutions are applicable for other instruments
Incorporate multi-frequency, multi-messenger astrophysics
Provide a framework to coordinate and schedule multiple facilities.

## Slide 19: Results: task 1
  Moving ahead at full speed, right from the start
    Has made real impact in WR community
      Improvements are fed back: open source
    Generated serious outside interest: JVLA
    Some delay with one partner, but no risk to project
      Has ramped up effort
    Fed into tender for new photonic equipment for SURFnet(8)
    WR timing in design of SKA-low
      Frequency stability now good enough for frequency transfer
    Commercial applications under development

## Slide 20: Results: task 2
  Task 2: slow uptake
    Speed-up since last change of task lead
    Draft of first deliverable document
    Some delay, but no risk to project timeline
      Will fit comfortably within the 4 years
    Active involvement of several astronomers interested in triggered observations
    Interactions with Work Package 4 and Cleopatra task 4
    MoU JIVE-EVN and LIGO regarding follow-up observations

## Slide 21: Results: task 3
  Fairly small task, one developer
    Prototype milestone reached well on time
    First tests very promising
      4Gbps file transfers from New Zealand to the Netherlands
    Now re-writing Python into C++11

## Slide 22: Results: task 4
  Excellent progress, from the start
    Several face to face meetings
    GTD had to change status from third party to full member
    Deliverables late in project:
      Intermediate milestones defined

## Slide 23: Outlook
  No major obstacles or deviations: on track
  Task 2: most delayed, but high potential
    Transient astronomy becoming more important (GW!)
    Real need in community for standards, implementation of filters, protocols
  Task 3: small, but could deliver something very useful
  Tasks 1 and 4: clear use cases, big impact
  Several demos coming up, good PR
  Results feed back into commercial applications

## Slide 24: `